## Slide 1: Smart and Intelligent Textiles: Software

## Slide 2: Smart and Intelligent Textiles- SOFTWARE
Following software will be used.
  Inkscape
  Ink/Stitch
  Arduino
  Google Chrome for online tools (python, arduino, DOE)

## Slide 3: InkScape
2D-Drawing
Vector Drawing Program
Open Source (GPL)
Install from the website: https://inkscape.org/
Notes: Inkscape
Adobe illustrator
CorelDraw
Macromedia Freehand
Affinity Designer
Microsoft Visio
Xara Extreme
Xfig

## Slide 4: InkScape
Creates Vector Drawings

## Slide 5: InkScape Interface
New page
Standard figures
Drawing lines (free hand)
Straight & Bend Lines (smooth)
Select Object selecteren, move, deform/scale
Change Lines
Text & Fonts

## Slide 6: Inkscape: used for ...
Images/icons … export in the dpi you want

## Slide 7: Inkscape: used for ...
CNC tools
  lasercutter
  vinyl cutter
  ...
fast
faster
slow
cut
engrave
raster

## Slide 8: Ink/Stitch
Add on for Inkscape
Used for digital embroidery
Inkscape 1.x+ MUST be installed
Installeer with the manual after selecting your computer system https://inkstitch.org/docs/install/
Restart Inkscape and test if all was installed
See option in Extensions:

## Slide 9: Ink/Stitch installation problems
Problem recent Mac: https://codewithhugo.com/catalina-permission-command-line-fix/ so do: xattr -d com.apple.quarantine /Applications/<app-name>.app
xattr -r -d com.apple.quarantine ~/Library/Application\ Support/org.inkscape.Inkscape/config/inkscape/extensions/
Problem Windows antivirus: ink/stitch uses same packaging methods as some malware, creating false positive hits as malware. See https://github.com/inkstitch/inkstitch/issues/710 or https://github.com/pyinstaller/pyinstaller/issues/4633
You must take inkstitch.exe then out of quarantaine so it would work (via Protection History). Then restart inkscape, if needed, copy inkstitch.exe to the correctlocation

## Slide 10: Ink/Stitch workflow
Draw
Generate Embroidery parameters
Verify the results - Improve

## Slide 11: Arduino
For intelligent textile projects, microcontrollers must be programmed
Do this through the Arduino IDE
Download from the site https://www.arduino.cc/en/software
Current version 1.8.15
Install via the option Windows Win 7 and newer , not via Win App.

## Slide 12: Arduino IDE
Texteditor
Compiler/Debugger
Linker/Locater
Bootloader
Serial monitor
Integrated Development Environment

## Slide 13: Google Chrome
Modern browser, allows for:
python programming through https://colab.research.google.com/
Basic electronics through 3dcircuits on https://www.tinkercad.com/
Visual Arduino programming

## Slide 14: Ink/Stitch: Smart Textile construction
Benny Malengier
Images from UWB, Czech Republic (OptimTex project cases)

## Slide 15: Ink/Stitch
Design patterns for use on embroidery machines

## Slide 16
Embroidery Stitch File Format | Embroidery Machine Brand
.ART | Bernina
.PES / .PEC | Brother / Baby Lock / Deco
.DST | Tajima / Barudan
.EXP | Melco / Bravo
.SEW / .JEF | Janome
.VP3 / .HUS / .VIP | Husqvarna /Viking
A list of machine embroidery file formats and machine brands

## Slide 17: Connections and pads with Ink/Stitch

## Slide 18: Embroider pads for electronic components
A possible design (in mm) is the following:
We require a way to embroider these pads. Step 1 is drawing them in the correct size with Inkscape

## Slide 19
Open Inkscape, and draw the rectangles, give then correct size

## Slide 20
With Ink/Stitch generate the embroidery pattern: Extension Ink/Stitch→ Params
Visualize, and embroider: Extensions → Ink / Stitch → Visualize and Export → Embroider…

## Slide 21: Assignment
A good assignment is to have students create the optimal pad for a component you give them.
Eg, for an SMD LED 1206 (mm dimension) it could be:

## Slide 22: Always use rectangular patch ?
If the accuracy of the gap is very important, then use manual hatching!
Remove the rectangle before embroidery

## Slide 23: Testing a good distance
Have students test with best distance, by embroidering different ones and see what works.

## Slide 24: Snap buttons
Consider larger pads for eg snap buttons or magnets.
Example: 10x10mm

## Slide 25: Arduino - Programming for Smart Textiles - Hands On
Benny Malengier

## Slide 26: What is Arduino ?
Arduino is an open source computer platform, meant to make the use of a microcontroller easy.
Arduino is for students, hobbyists, artists, and everybody interested in the making of “smart” and “creative” objects.

## Slide 27
2005: the first!
2009: USB !
2017: Arduino UNO (Rev. 03)

## Slide 28: What can you do with Arduino?
Measurement/input → Think (software) → Output: sound, light, action, display, ...

## Slide 29: What is inside an Arduino UNO ?

## Slide 31: Arduino IDE
Integrated Development Environment
Texteditor
Compiler/Debugger
Linker/Locater
Bootloader
Serial monitor
Download from: https://www.arduino.cc/en/Main/Software
Free software (Linux, OSX, Windows) - Current version 1.8.15

## Slide 32: IDE - Settings
To compile an Arduino sketch (= program) correctly, the IDE must know which type of Arduino (= board) is being used,
To be able to upload a sketch to the Arduino, the IDE must know via which port the Arduino is connected with the PC.

## Slide 33: What is a sketch ?
A sketch is an Arduino programm,
A sketch is saved in a folder with the same name as the sketch,
A sketch can be made/edited with the Arduino IDE.
Not used to programming? You can use several block based environments to create code. We use: blokkencode.ingegno.be/index_en.html

## Slide 34: What is in a sketch ?
a sketch contains at least always the following 2 unique functions:
  void setup()
    Takes care of the initialisation,
    Is begin executed one single time,
      after power-up,
      after reset,
      after starting a serial monitor (introspection of the code),
  void loop()
    Contains the main program that executes again and again.

## Slide 35: A first program with Blocks
To start, we use an interactive programming environment: blokkencode.ingegno.be/index_en.html
Use index_en.html for the English version

## Slide 36: Minimum Sketch content
Load following minimum sketch to the Arduino

## Slide 37: Working with a LED
The Arduino has an internal LED on the board
This is connected with pin 13 on Arduino. On WEMOS use pin D4 instead
Make a LED blink:

## Slide 38
Coordinator:
Technical University of Sofia
Faculty of Power Engineering and Power Machines
Project Manager of ICT-TEX:
Assoc. Prof. Dr. Angel Terziev
е-mail: aterziev@tu-sofia.bg
Web-site: ICT-TEX.eu
Contact: Benny Malengier, PhD, DSc
benny.malengier@ugent.be
CONTACTS
The information and views set out in this publication are those of the authors and do not necessarily reflect the official opinion of the European Union. Neither the European Union institutions and bodies nor any person acting on their behalf may be held responsible for the use which may be made of the information contained therein.